## Slide 1: Design Example: Binary Multiplier
ECE 2372 | Modern Digital System Design | Texas Tech University

## Slide 2: Lecture Overview
Design Specification
Shift-Register
Adder
Control Circuit
System Integration

## Slide 3: Design Specification
Binary Multiplier | Modern Digital System Design

## Slide 4: Design Specification
Design a sequential circuit capable of performing multiplication on 4-bit binary numbers to get an 8-bit product.
Multiplication involves successive addition and shifting operations.

## Slide 5: Design Specification
1101
1011
(13)
(11)
Multiplicand
Multiplier

## Slide 6: Design Specification
1101
1011
00001101
(13)
(11)
Shift Left 0-bits
Multiplicand
Multiplier

## Slide 7: Design Specification
1101
1011
00001101
00011010
(13)
(11)
Shift Left 0-bits
Shift Left 1-bit
Multiplicand
Multiplier

## Slide 8: Design Specification
1101
1011
00001101
00011010
00100111
(13)
(11)
Shift Left 0-bits
Shift Left 1-bit
Add
Multiplicand
Multiplier

## Slide 9: Design Specification
1101
1011
00001101
00011010
00100111
00000000
(13)
(11)
Shift Left 0-bits
Shift Left 1-bit
Add
Zeros
Multiplicand
Multiplier

## Slide 10: Design Specification
1101
1011
00001101
00011010
00100111
00000000
00100111
(13)
(11)
Shift Left 0-bits
Shift Left 1-bit
Add
Zeros
Add
Multiplicand
Multiplier

## Slide 11: Design Specification
1101
1011
00001101
00011010
00100111
00000000
00100111
01101000
(13)
(11)
Shift Left 0-bits
Shift Left 1-bit
Add
Zeros
Add
Shift Left 3-bit
Multiplicand
Multiplier

## Slide 12: Design Specification
1101
1011
00001101
00011010
00100111
00000000
00100111
01101000
10001111
(13)
(11)
Shift Left 0-bits
Shift Left 1-bit
Add
Zeros
Add
Shift Left 3-bit
Add
Multiplicand
Multiplier
(143)

## Slide 13: Design Specification
We’ll need to design 5 components
  A 4-bit shift register to hold the multiplier
  A 5-bit shift register to hold the multiplicand
    The product will come from the multiplier register and the least 4-bits of the multiplicand register.
  4-bit binary adder
    Good old-fashioned ripple-carry adder.
  Control Circuit

## Slide 14: Design Specification
Multiplier
(B)
>
>
SO
SI
SI
Multiplicand
(A)
Binary
Adder
Control
LD
SH
AD
>
Done
ST
M
LD
SH
LD
SH
Product

## Slide 15: What questions do you have?

## Slide 16: Shift Registers
Binary Multiplier | Modern Digital System Design

## Slide 17: Shift Registers
For the two shift registers, we’ll implement the same PIPO registers that we’ve used previously.

## Slide 19: What questions do you have?

## Slide 20: Binary Adder
Binary Multiplier | Modern Digital System Design

## Slide 21: Binary Adder
For the binary adder, we’ll simply implement a 4-bit ripple-carry adder.

## Slide 25: What questions do you have?

## Slide 26: Control Circuit
Binary Multiplier | Modern Digital System Design

## Slide 27: Control Circuit
>
>
BINARY COUNTER
CONTROLLER
ST
M
SH
LD
AD
EN
DONE

## Slide 28: Control Circuit: Counter
We need to count that a shift has occurred 4 times.
We’ll implement a synchronous binary counter.

## Slide 29: Control Circuit: Counter
Notes: Notice that the DONE signal is just an AND of both state bits.

## Slide 30: Control Circuit: Counter
Notes: Notice that the DONE signal is just an AND of both state bits.

## Slide 31: Control Circuit
The controller circuit will need to manage the behavior of the shift registers to ensure that the multiplication algorithm is followed.

## Slide 32
REST
ADD
SHIFT
LOAD
ST, M, D/EN, LD, AD, SH

## Slide 33
REST
ADD
SHIFT
LOAD
0XX/0000
ST, M, D/EN, LD, AD, SH

## Slide 34
REST
ADD
SHIFT
LOAD
0XX/0000
1XX/0100
ST, M, D/EN, LD, AD, SH

## Slide 35
REST
ADD
SHIFT
LOAD
ST, M, D/EN, LD, AD, SH
0XX/0000
1XX/0010
X0X/1001

## Slide 36
REST
ADD
SHIFT
LOAD
ST, M, D/EN, LD, AD, SH
0XX/0000
1XX/0010
X0X/1001
X1X/0010

## Slide 37
REST
ADD
SHIFT
LOAD
ST, M, D/EN, LD, AD, SH
0XX/0000
1XX/0010
X0X/1001
X1X/0010
XXX/1001

## Slide 38
REST
ADD
SHIFT
LOAD
ST, M, D/EN, LD, AD, SH
0XX/0000
1XX/0010
X0X/1001
X1X/0010
XXX/1001
X00/1001

## Slide 39
REST
ADD
SHIFT
LOAD
ST, M, D/EN, LD, AD, SH
0XX/0000
1XX/0010
X0X/1001
X1X/0010
XXX/1001
X00/1001
X10/0010

## Slide 40
REST
ADD
SHIFT
LOAD
ST, M, D/EN, LD, AD, SH
0XX/0000
1XX/0010
X0X/1001
X1X/0010
XXX/1001
X00/1001
X10/0010
XX1/0000

## Slide 41: Control Circuit
This circuit has 3 inputs and 4 states (2 Flip-Flops).
This means that our next-state and output equations will be Boolean functions of 5 variables.
We have two options:
  Try and reduce the input space by 1
  Utilize a different design pattern.

## Slide 43
We can hard-code our state table using case syntax.
This is great for sequential circuits that are too large for our traditional design pattern.
However, we must hardcode each entry in the table.
We’d like to use some don’t cares.

## Slide 44
REST
ADD
SHIFT
LOAD
ST, M, D/EN, LD, AD, SH
0XX/0000
1XX/0010
X0X/1001
X1X/0010
XXX/1001
X00/1001
X10/0010
XX1/0000

## Slide 46: System Integration
Binary Multiplier | Modern Digital System Design

## Slide 47: Design Specification
Multiplier
(B)
>
>
SO
SI
SI
Multiplicand
(A)
Binary
Adder
Control
LD
SH
AD
>
Done
ST
M
LD
SH
LD
SH
Product

## Slide 50: What questions do you have?

## Slide 51: Lecture Recap
Design Specification
Shift-Register
Adder
Control Circuit
System Integration

## Slide 52: What questions do you have?

## Slide 53: Design Example: Binary Multiplier
ECE 2372 | Modern Digital System Design | Texas Tech University